## Slide 1
ASSEMBLY INSTRUCTIONS POOLDECK

## Slide 2
FOREWORD
We congratulate you on the purchase of your Pooldeck pool enclosure.
This enclosure has been designed to ensure that you are fully satisfied, both when assembling it and when using it.
To ensure that you are fully satisfied, we recommend that you read and follow the assembly instructions carefully:
- These diagrams are established as examples and in no way replace official documents such as standards, professional recommendations, codes of practice, industry practices, etc.
- It is the responsibility of the person installing the enclosure to ensure that these standards are met;
we will not be held responsible for any incorrect installation or technical misuse of our products,
- Any modifications, even partial, involving a product that is not from
"AZENCO GROUP" shall exempt the latter from any civil, criminal, financial and legal liability.
Avoid assembling your enclosure in wet or windy conditions.
- Do not install your enclosure directly under a power line.
- Avoid placing tools on the upper parts of the enclosure when assembling it.
- You must also ensure that children are kept away from the enclosure during assembly to avoid the risk of them falling from a ladder, being injured by sharp tools, etc.
- Even if you do not plan to assemble your enclosure immediately after purchase, we recommend that you take the time to unpack the enclosure, check that all parts are present (using the parts list) and that none of them are damaged or broken. If you find that a part is missing or damaged, or if you encounter any problems when assembling your enclosure, please contact our after-sales team. They will deal with your request as soon as possible.
Please keep all documents concerning your enclosure (instructions, invoice, etc.) for future reference; you will need them if you contact us at a later date.
EQUIPMENT REQUIRED (not supplied)
Drill Tape measure Allen key
12mm and 6mm concrete drill bits Mallet/Hammer

## Slide 3
2
PART N° | DESCRIPTION |  | QTY
1 | BEAM |  | X
2 | CONNECTING BRACKET |  | X
3 | BRUSH SEAL - SWJ055 |  | X
4 | WHEEL SUPPORT BRACKET |  | X
6 | WHEEL |  | X
7 | AP14 beam |  | X
ASSEMBLY - PARTS LIST

## Slide 4
2
PART N° | DESCRIPTION |  | QTY
8 | I-SHAPED CROSS BEAM |  | X
9 | STARTER CLIP |  | X
10 | JOINING CLIP |  | X
11 | FLOOR SLAT |  | X
12 | ALUMINIUM EDGING STRIP |  | X
13 | CORNER PIECE |  | X
14 | SCREW COVER - SWQ262 |  | X
15 | CLIPS |  | X
ASSEMBLY - PARTS LIST

## Slide 5
2
PART N° | DESCRIPTION |  | QTY
16 | GUIDE |  | X
17 | STOP BLOCK - SWQ20 |  | X
18 | LOCKING HOOK |  | X
19 | VERINOX DROP PIN |  | X
20 | SWQ7055 |  | X
21 | SCREW (4.8 x 25) |  | X
22 | BOLT (M8 x 75) + NUT |  | X
ASSEMBLY - PARTS LIST

## Slide 6
2
PART N° | DESCRIPTION |  | QTY
23 | SET SCREW (M10 x 20mm) |  | X
24 | SCREW PLUG (M10 x 60mm) |  | X
25 | SCREW PLUG (M6 x 60mm) |  | X
26 | SCREW (5 x 50) |  | X
27 | COUNTERSUNK SELF-DRILLING SCREW (3.9 x 19) |  | X
28 | DECK SEAL 02 |  | X
29 | COUNTERSUNK SELF-DRILLING SCREW (4.8 x 50) |  | X
30 | ROUND-HEAD SELF-DRILLING SCREW (4.8 x 50) |  | X
ASSEMBLY - PARTS LIST

## Slide 7
2
PART N° | DESCRIPTION |  | QTY
31 | MOTOR |  | X
32 | SOLAR PANEL |  | X
33 | SEAL - SWJ010001 |  | X
34 | WHEEL SUPPORT BRACKET #2 |  | X
ASSEMBLY - PARTS LIST

## Slide 8
STEP 1 Place the Pooldeck beams that will not be fitted with wheels on the trestles
OPTION 1: The Pooldeck travels lengthways, so the wheels should be positioned on the longest beams
OPTION 2: The Pooldeck travels widthways, so the wheels should be positioned on the shorter beams
If your Pooldeck is longer than 5m, the beams are slightly curved
ASSEMBLY – POOLDECK

## Slide 9
ASSEMBLY – POOLDECK
A
B
Beam
Beam

## Slide 10
STEP 2
Position the connecting brackets on the ends of the beams
STEP 3
Screw in place with the 4.8x25 screws
ASSEMBLY – POOLDECK
A
B
A
B
Connecting bracket
Beam
Screw (4.8x25)

## Slide 11
STEP 4
Repeat steps 2 and 3 as shown below:
ASSEMBLY – POOLDECK

## Slide 12
STEP 5
Position the brush seal - SWJ055
ASSEMBLY – POOLDECK
SWJ055
Beam
A
B
SWJ055
SWJ055
Beam
Connecting bracket
If the deck height is 100, you will need to substitute the SWJ010001 seal for the SWJ055 brush seal

## Slide 13
ASSEMBLY – POOLDECK
C
D
E

## Slide 14
ASSEMBLY – POOLDECK
F

## Slide 15
ASSEMBLY – POOLDECK
STEP 6
Place the remaining 2 beams (which are to be fitted with wheels) on trestles

## Slide 16
ASSEMBLY – POOLDECK
STEP 7
Position the wheel support bracket + wheel at the end of the beam
A
B
Beam
Wheel support bracket
wheel
If the deck height is 100, use the wheel support bracket #2 (see parts list)

## Slide 17
ASSEMBLY – POOLDECK
STEP 8
Fix the wheel support + wheel to the beam using the 8x75 bolts
A
B
Bolt (8x75)

## Slide 18
ASSEMBLY – POOLDECK
C
D
Nut

## Slide 19
ASSEMBLY – POOLDECK
STEP 8
Screw the wheel support to the beam using the 4.8x25 screws
Screw (4.8x25)

## Slide 20
ASSEMBLY – POOLDECK
STEP 9
Repeat on the other side

## Slide 21
ASSEMBLY – POOLDECK
STEP 10
Slide the SWJ055 seal into the beams
A
B
SWJ055
Brush (50)

## Slide 22
ASSEMBLY – POOLDECK
C
D

## Slide 23
ASSEMBLY – POOLDECK
D

## Slide 24
ASSEMBLY – POOLDECK
STEP 11
Position the first beam (from step 1) on the ground
STEP 12
Position the AP14 beams
A
A
AP14 beam
Beam

## Slide 25
ASSEMBLY – POOLDECK
B
C

## Slide 26
ASSEMBLY – POOLDECK
STEP 13
Screw in place using the 4.8x25 screws
A
B
Screw (4.8x25)

## Slide 27
ASSEMBLY – POOLDECK
C
STEP 14
Attach the second beam to the AP14 beam

## Slide 28
ASSEMBLY – POOLDECK
STEP 15
Add the first beam (fitted with wheels in step 6)
A
B
Beam
with wheels
Beam
with wheels
Beam
without wheels

## Slide 29
ASSEMBLY – POOLDECK
C
D

## Slide 30
ASSEMBLY – POOLDECK
STEP 16
Screw in place using the 4.8x25 screws
A
B
Screw (4.8x25)

## Slide 31
ASSEMBLY – POOLDECK
STEP 17
Repeat on the other side

## Slide 32
ASSEMBLY – POOLDECK
STEP 18
Position the I-shaped cross beam between the beam and the AP14 beams
A
B
I-SHAPED CROSS BEAM
AP14 beam
Beam

## Slide 33
ASSEMBLY – POOLDECK
C
D
Pre-drilled hole
I-SHAPED CROSS BEAM

## Slide 34
ASSEMBLY – POOLDECK
STEP 19
Screw the I-shaped cross beam in place with the 4.8x25 screws
A
B
Screw (4.8x25)

## Slide 35
ASSEMBLY – POOLDECK
C
D

## Slide 36
ASSEMBLY – POOLDECK
STEP 20
Repeat for the other cross beams
E

## Slide 37
ASSEMBLY – POOLDECK
If the length of your Pooldeck is less than 5m, skip to step 21

## Slide 38
ASSEMBLY – POOLDECK
STEP 20.1
Position the 4 reinforcement plates 30 cm from the edge of the Pooldeck
The reinforcement plates are to be positioned on the two shorter sides of the Pooldeck
30cm

## Slide 39
ASSEMBLY – POOLDECK
STEP 20.2 Drill the holes as shown below:
To make things easier, we have assigned a letter to each hole:
Ø 4 mm
Ø 4 mm
Ø 4 mm
Ø 22 mm
A
B
C
D

## Slide 40
ASSEMBLY – POOLDECK
STEP 20.3 Screw the reinforcement plate to the Pooldeck beam using the 4.8 x 25 round-head self-drilling screws at holes B / C and D
4.8x25 screws

## Slide 41
ASSEMBLY – POOLDECK
STEP 20.4
Slide the male tie rod through hole A in the reinforcement plate

## Slide 42
ASSEMBLY – POOLDECK
STEP 20.5
Slide the female tie rod through hole A in the reinforcement plate (reverse side)

## Slide 43
ASSEMBLY – POOLDECK

## Slide 44
ASSEMBLY – POOLDECK
STEP 20.6
Attach the two tie rods using a Ø14mm bolt, 2 x Ø30mm washers and a lock nut
Ø14mm bolt
Lock nut
Ø30mm washer
Ø30mm washer

## Slide 45
ASSEMBLY – POOLDECK
STEP 20.7
Attach the two tie rods to the reinforcement plates using a Ø40mm washer and a Ø22mm bolt
Tie rod
Ø40mm washer
Ø22 bolt
Reinforcement
plate

## Slide 46
ASSEMBLY – POOLDECK
STEP 20.8 Repeat on each side

## Slide 47
ASSEMBLY – POOLDECK
STEP 20.9 Cut the tie rod flush with the bolt

## Slide 48
ASSEMBLY – POOLDECK
STEP 21
Measure 10mm around the edge all around of the Pooldeck

## Slide 49
ASSEMBLY – POOLDECK
10mm
10mm

## Slide 50
ASSEMBLY – POOLDECK
STEP 22
Position the starter clip at the corner of the Pooldeck (on the line that you marked 10 mm from the edge in step 21)
A
B
Starter clip

## Slide 51
ASSEMBLY – POOLDECK
STEP 23
Screw in place with a 3.9x19 countersunk self-drilling screw
A
B
Countersunk self-drilling screw (3.9x19)

## Slide 52
ASSEMBLY – POOLDECK
STEP 24
Repeat this opposite each I-shaped cross beam and at the remaining corner

## Slide 53
ASSEMBLY – POOLDECK
Starter
clip

## Slide 54
ASSEMBLY – POOLDECK
STEP 25
Position the first floor slat
A
Floor slat

## Slide 55
ASSEMBLY – POOLDECK
STEP 26
Position the next joining clips against the floor slat, respecting the 10mm gap around the edge
B
A
Starter
clip

## Slide 56
ASSEMBLY – POOLDECK
STEP 27
Screw in place with a 3.9x19 countersunk self-drilling screw
B
A
Countersunk self-drilling screw (3.9x19)

## Slide 57
ASSEMBLY – POOLDECK
STEP 28
Place the joining clip on the I-shaped cross beam
B
A
Joining
clip

## Slide 58
ASSEMBLY – POOLDECK
B
C

## Slide 59
ASSEMBLY – POOLDECK
STEP 29
Screw in place with a 3.9x19 countersunk self-drilling screw
A
B
Screw (3.9x19)
COUNTERSUNK SELF-DRILLING SCREW

## Slide 60
ASSEMBLY – POOLDECK
STEP 30
Repeat for all of the cross beams
Floor slat
Starter clip

## Slide 61
ASSEMBLY – POOLDECK
STEP 31
Position the next floor slat
Floor slat 1
Floor slat 2

## Slide 62
ASSEMBLY – POOLDECK
STEP 32
Repeat steps 26 to 31 until the entire surface of the Pooldeck is covered
FOR THE LAST SLAT
Position the last floor slat

## Slide 63
ASSEMBLY – POOLDECK
Draw a line for cutting the slat to the required size - keeping the 10mm gap at the edge
Cut the slat and re-position it
10mm

## Slide 64
ASSEMBLY – POOLDECK
Screw in place with a 3.9x19 countersunk self-drilling screw
Countersunk self-drilling screw (3.9x19)

## Slide 65
ASSEMBLY – POOLDECK
STEP 33
Position the starter clips on the beam 5cm from the edge
A
B
5cm
Starter clip

## Slide 66
ASSEMBLY – POOLDECK
STEP 34
Screw in place with a 3.9x19 countersunk self-drilling screw
A
B
Countersunk self-drilling screw (3.9x19)

## Slide 67
ASSEMBLY – POOLDECK
STEP 35
Repeat every 50cm
50cm

## Slide 68
ASSEMBLY – POOLDECK
STEP 36
Position the floor slat on the starter clips
Floor slat
Starter clip

## Slide 69
ASSEMBLY – POOLDECK

## Slide 70
ASSEMBLY – POOLDECK
STEP 36.1
If your Pooldeck is longer than 5m, cut out a section of the floor slat to make room for the bolt:

## Slide 71
ASSEMBLY – POOLDECK

## Slide 72
ASSEMBLY – POOLDECK
STEP 37
Fix the floor slat to the beam using a 3.9x19 countersunk screw every 50cm
Countersunk self-drilling screw (3.9x19)

## Slide 73
ASSEMBLY – POOLDECK

## Slide 74
ASSEMBLY – POOLDECK
50cm
50cm
50cm

## Slide 75
ASSEMBLY – POOLDECK
STEP 38
Repeat steps 33 to 37 all around the Pooldeck

## Slide 76
ASSEMBLY – POOLDECK
STEP 39
Position the aluminium edging strip as shown below
Aluminium edging strip
A
B
C

## Slide 77
ASSEMBLY – POOLDECK
STEP 40
Drill a Ø4mm hole 5cm from the edge
A
4mm drill bit
B

## Slide 78
ASSEMBLY – POOLDECK
C
D

## Slide 79
ASSEMBLY – POOLDECK
STEP 41
Screw in place with 4.8x25 screws
A
B
Screw (4.8x25)

## Slide 80
ASSEMBLY – POOLDECK
C

## Slide 81
ASSEMBLY – POOLDECK
STEP 42
Repeat every 50cm
STEP 43
Repeat steps 39 to 42 all around the Pooldeck
50cm
Aluminium edging strip

## Slide 82
ASSEMBLY – POOLDECK
Aluminium edging strip
Aluminium edging strip

## Slide 83
ASSEMBLY – POOLDECK
Aluminium edging strip

## Slide 84
ASSEMBLY – POOLDECK
STEP 44
Position the corner piece at the corner of the Pooldeck
A
B
Corner piece

## Slide 85
ASSEMBLY – POOLDECK
STEP 45
Drill a Ø 4mm hole in the centre of the edging strip and the corner piece
A
B
4mm drill bit

## Slide 86
ASSEMBLY – POOLDECK
STEP 46
Repeat on the second side of the corner piece
A
B
C

## Slide 87
ASSEMBLY – POOLDECK
STEP 47
Screw the corner piece in place using the 4.8x50 screws
A
B
Screw (4.8x50)

## Slide 88
ASSEMBLY – POOLDECK
STEP 48
Fit the SWQ262 screw covers
A
B
SWQ262

## Slide 89
ASSEMBLY – POOLDECK
STEP 49
Repeat steps 44 to 48 on all 4 corners of your Pooldeck

## Slide 90
ASSEMBLY – POOLDECK
STEP 50
Position the clips on the aluminium edging strip
A
B
C
D
Clips
Clips
Aluminium edge profile

## Slide 91
ASSEMBLY – POOLDECK
STEP 51
Pre-drill the guide rail to Ø 5mm at 5cm from the edge and drill a hole every 50cm
5cm
50cm
50cm
50cm
A
B
5mm drill bit
C
D
Rail

## Slide 92
ASSEMBLY – POOLDECK
STEP 52
Drill Ø 10mm holes in the guide rail
A
B
C
D
10mm drill bit
Rail

## Slide 93
ASSEMBLY – POOLDECK
STEP 53
Position the guide rail on the ground
E

## Slide 94
ASSEMBLY – POOLDECK

## Slide 95
ASSEMBLY – POOLDECK
STEP 54
Drill a Ø 6mm hole in the ground
6mm drill bit

## Slide 96
ASSEMBLY – POOLDECK
STEP 55
Using a hammer, fix the rail to the ground using the screw plugs and 4.8x50 screws
Screw (4.8x50)
Screw plug

## Slide 97
ASSEMBLY – POOLDECK

## Slide 98
ASSEMBLY – POOLDECK
STEP 56
Position the SWQ20 stop block at both ends of the rail, as close as possible to the wheel
SWQ20

## Slide 99
ASSEMBLY – POOLDECK
STEP 57
Measure
STEP 58
Move the Pooldeck and re-position the stop block to the correct distance, and pre-drill the rail to Ø 4mm
4mm drill bit

## Slide 100
ASSEMBLY – POOLDECK
STEP 59
Fix in place with screw plugs and 5x50 screws
Screw (5x50)
Screw plug

## Slide 101
ASSEMBLY – POOLDECK
STEP 60
Move the Pooldeck and repeat this process at the other end of the rail

## Slide 102
ASSEMBLY – POOLDECK
SWQ20

## Slide 103
ASSEMBLY – POOLDECK

## Slide 104
ASSEMBLY – POOLDECK
STEP 61
Position the locking hook 5cm from the edge
Locking hook

## Slide 105
ASSEMBLY – POOLDECK
STEP 62
Drill 4 holes of the hook to Ø 4mm
4mm
drill bit

## Slide 106
ASSEMBLY – POOLDECK

## Slide 107
ASSEMBLY – POOLDECK
STEP 63
Screw in place with the 4.8x25 screws
Screw (4.8x25)

## Slide 108
ASSEMBLY – POOLDECK
STEP 64
Repeat on the other side
USE THE HANDLING POLE TO MOVE THE POOLDECK

## Slide 109
ASSEMBLY – POOLDECK
STEP 65
Position the Verinox drop pin support 25 cm from the edge
25cm
Verinox drop pin support

## Slide 110
ASSEMBLY – POOLDECK
STEP 66
Using a 4mm drill bit, drill a hole through the Verinox drop pin support & the Pooldeck frame
STEP 67
Screw in place with the 4.8x50 screws
4mm drill bit

## Slide 111
ASSEMBLY – POOLDECK
STEP 68
Slide the Verinox drop pin into its support
STEP 69
Position the Verinox cover
Stainless-steel
drop pin
Cover verinox drop pin

## Slide 112
ASSEMBLY – POOLDECK
STEP 70
Screw the cover in place using the screws provided
STEP 71
Mark the position of the drop pin on the ground as shown below:

## Slide 113
ASSEMBLY – POOLDECK
STEP 72
Lift the Verinox drop pin
STEP 73
Move the Pooldeck
Stainless-steel
drop pin
Ground marking

## Slide 114
ASSEMBLY – POOLDECK
STEP 74
Drill a hole in the ground using a 12mm drill bit
STEP 75
Place a 10x60 screw plug and a 10x20 set screw in the hole
12mm drill bit
Ground marking
Screw plug
Set screw

## Slide 115
ASSEMBLY – POOLDECK
STEP 76
Reposition the Pooldeck and screw the Verinox drop pin to the ground to lock the Pooldeck in place

## Slide 116
ASSEMBLY – POOLDECK
STEP 77
Repeat steps 65 to 76 on the other side of the Pooldeck

## Slide 117
ASSEMBLY – POOLDECK
STEP 78
IF YOU HAVE A SECOND DECK:
Position the second deck
Second deck

## Slide 118
ASSEMBLY – POOLDECK
Stick the deck seal 02 (self-adhesive) on one of the deck clips
Deck seal 02

## Slide 119
ASSEMBLY – POOLDECK
Bring the 2 Pooldeck decks together
Position the SWQ7055 latch as shown below:
SWQ7055
Deck seal 02
DECK 2
DECK 1

## Slide 120
ASSEMBLY – POOLDECK
Drill the SWQ7055 with a 4mm drill bit
4mm drill bit

## Slide 121
ASSEMBLY – POOLDECK
Screw in place with the 4.8x50 round-head self-drilling screws
Round-head self-drilling screw (4.8x50)

## Slide 122
ASSEMBLY – POOLDECK
Extend the SWQ7055 rod as far as possible and position the SWQ7055 latch hook
SWQ7055 latch hook

## Slide 123
ASSEMBLY – POOLDECK
Drill with a 4mm drill bit
Screw in place with the 4.8x50 countersunk self-drilling screws
4mm drill bit
Countersunk self-drilling screws (4.8x50)

## Slide 124
Reposition the rod of the SWQ7055 and hook it in place
ASSEMBLY – POOLDECK

## Slide 125
Close the SWQ7055 latch
Repeat on the other side
ASSEMBLY – POOLDECK

## Slide 126
ASSEMBLY – POOLDECK
STEP 79
IF YOUR POOLDECK IS FITTED WITH A MOTOR (on both sides):
Position the Pooldeck motor
Motor

## Slide 127
ASSEMBLY – POOLDECK
Drill with a 4mm drill bit
Screw in place with the 4.8x50 round-head self-drilling screws
4mm drill bit
Round-head self-drilling screw (4.8x50)

## Slide 128
ASSEMBLY – POOLDECK
Remove the clips and insert the motor cable
Motor
Motor cable

## Slide 129
Fit the solar panel
ASSEMBLY – POOLDECK
Make the necessary connections according to the connection instructions supplied with the motor
Solar panel

## Slide 130
Note: Route the solar panel cables with the motor cables (behind the clips)
Re-fit the clips
Fit the motor cover
ASSEMBLY – POOLDECK
Clips
Cover

## Slide 131
ASSEMBLY – POOLDECK